## Slide 1
UIUC RIPE · HYPERSPECTRAL ANALYSIS
From field hyperspectral data
to research-ready results
CERES/BIL → Reflectance calibration → Clustering → ROI spectra → Automated reports
Field-scale hyperspectral analysis workflow
Notes: Suggested presentation script
Today I will introduce a workflow that turns large field hyperspectral datasets into research-ready results.
The pipeline loads CERES or BIL data, converts raw measurements to reflectance using a white panel and sensor dark, performs clustering and ROI analysis, and generates automated reports.
The goal is not to add more complicated options. It is to help the research team review repeated field measurements quickly, consistently, and with a clear record of the processing decisions.
The next slide summarizes the workflow in five steps.
[Sources]
- Internal project workflow based on user-provided requirements.
[/Sources]

## Slide 2
Five steps turn field data into research results
The workflow every user needs to remember
1
Load data
Select a CERES entry
or open BIL/HDR
2
Calibrate
White panel +
Sensor dark
3
Cluster
Leaves · soil · shadow
Whole-image separation
4
Inspect ROI
Review color overlay
and define regions
5
Export
HTML · Excel · CSV
images · daily summary
Default clustering input: normalized Raw DN
Final output includes QC-approved calibrated reflectance
02
Notes: Suggested presentation script
The workflow has five main steps.
First, we select an acquisition inside a CERES file or open an existing BIL and HDR dataset. Second, we apply reflectance calibration using a white panel and the sensor dark signal.
Third, we cluster the full image to separate leaves, soil, shadows, and strongly illuminated regions. Fourth, we inspect the color overlay on the RGB preview and define the regions of interest. Finally, we save the results as HTML, Excel, CSV, and image files, and we can also generate a daily summary across plots.
One important distinction is that normalized Raw DN is the recommended default for clustering, while research-ready spectra and vegetation indices also include the QC-approved calibrated reflectance.
[Sources]
- Internal project workflow based on user-provided requirements.
[/Sources]

## Slide 3
Validate calibration, then reanalyze only failed ROIs
1 · INPUT & CALIBRATION
2 · GLOBAL ANALYSIS
3 · ROI & REPORT
Select data
CERES entry or BIL/HDR
White + Dark
Panel ROI and sensor dark
calibration.npz + QC
Saturation · 800 nm steps
Valid wavelengths · continuity
RGB / Quick preview
Preview large scenes first
Choose analysis data
Default: normalized Raw DN
Optional: calibrated reflectance
Global clustering
RGB + overlay verifies
leaf · soil · shadow separation
Define ROI
Box or polygon regions
Quality check
Good → extract
Poor → recluster the ROI
Save results
Raw + calibrated spectra
HTML · Excel · CSV · PNG
per-file + daily summaries
QC-approved calibration.npz → final spectra and vegetation indices use calibrated reflectance
03
Notes: Suggested presentation script
In more detail, the workflow has three operational sections: input and calibration, global analysis, and ROI-based reporting.
We begin by selecting a CERES entry or a BIL dataset. The calibration profile is created from the white-panel measurement and sensor dark. Before it is accepted, the software checks for saturated bands, step-like discontinuities near 800 nanometers, valid wavelength coverage, and overall spectral continuity.
For a large scene, we first use a quick RGB preview and then run global clustering. The RGB image and cluster overlay are reviewed together to confirm that leaves, soil, shadows, and bright regions are separated appropriately.
If the result is satisfactory, spectra are extracted for the selected ROIs. If only one region performs poorly, we recluster that ROI with its own settings instead of repeating the analysis for the entire scene.
The final output preserves both raw and calibrated spectra and produces per-file reports as well as a daily summary. This keeps the analysis traceable while reducing unnecessary computation.
[Sources]
- Internal project workflow based on user-provided requirements.
[/Sources]